# The MIRAC Instruction Set
Version 1.4

## Introduction
This document describes in detail the instruction set of the MIRAC Minecraft Redstone Automatic Computer as well as syntax and structure of the MIDAS Assembly Language.
### Instruction Notation
Instructions are described as follows:

Mnemonic	Short Description	Binary	Oct	Argument 1	Argument 2
Microcode
Description

### Abbreviations

The following abbreviations are used:

Abbreviation	Full Form
A	Accumulator Register
PC	Program Counter Register
OP	ALU Operand Register
ABR	Address Bus Register
DIN	Data Bus In
DOUT	Data Bus Out
PABR	Periphery Address Bus Register
PDIN	Periphery Data Bus In
PDOUT	Periphery Data Bus Out
SP	Stack Pointer
GP0...GP7	General Purpose Registers 0 – 7
Z	Zero Flag
C	Carry Flag
O	Overflow Flag
N	Negative Flag
ALU	Arithmetic Logical Unit

## Architecture

## The Instruction Set
### Section I: Program flow

NOPE	Null Operation	00 000 000	000	-	-
PC ⇐ PC + 1
Do nothing and increment PC.

JMPA	Accumulator Jump	00 000 000	000	-	-
PC ⇐ A
Jump to memory location specified in Accumulator

## The MIDAS Assembly Language